# Airboad
Use some kind of way to measure finger positions of at least one full hand to use as a keyboard. Measurement needs to be independent of hand location, e.g. should work in free air – and be as unobtrusive as possible. Reasoning is about the same as for 'Tiprat', though 'Airboad' will be a lot more useful for e.g. mobile devices or google glasses (writing emails while walking around, anyone?). Also, when the absolute pose of the fingers can be detected (see IMU or RFID approaches below), the 'Tiprat' functionally comes for free, basically.
Current ideas are:
1. Dataglove-Like: Use what dataglove uses, i.e. some kind of optical fibres to measure the angles of the finger joints. Need to look more into dataglove to see if it's either possible to recreate, or if the interfaces are as flexible as needed for implementing a whole keyboard with that. Also the possibility to use two datagloves simultaneous needs to be evaluated.
2. IMU: Use one inertial movement sensor per finger – this is probably way too expensive! Also drift may be problematic, especially when relative position of fingers in respect to each other is of interest.
3. Short range distance sensing with triangulation: Use RFID-chips (or similar) for each finger tip, and an array (at least 3) of sensors at the wrist for triangulation. This method will heavily depend on the availability of sensor/chip combo to allow for robust and accurate short-range distance sensing.
4. Armband-thing-like: Sense finger/hand pose from electrical impulses at the muscles in the forearm. This is a little strange, but if it works (precisely enough!), will probably be the most comfortable solution.
Besides, it's planned to use vibration motors to induce some kind of haptic feedback, allowing to 'feel' the keys and especially key edges. Thus making it possible to know where one key ends and another begins. This is quite crucial, as it's intended to avoid any kind of visual feedback for that.